PHSCAN SERIES WATERPROOF POCKET pH TESTER

PHscan10S pocket pH tester is equipped with a standard pH electrode ( Round glass bulb ) that used to measures the pH of non-viscous, non-high temperature liquids, e.g., tap water, drinking water, rainwater, etc.

Features:
>2 points push-button calibration with auto-buffer recognition. 
>Hold function freezes the current displayed value for easy viewing and recording. 
>Auto-power off feature helps you effectively conserve battery life. 
>Replaceable electrode reduces maintenance and replacement cost. 
>Waterproof feature to ensures complete protection in harsh environments.

Specifications:

| Model No. | PHscan10S |
| --- | --- |
| pH Range | 0.0~14.0pH |
| pH Accuracy | ±0.1pH |
| Calibration Points | 2 points |
| Calibration Solutions | USA (pH4.01, 7.00, 10.01) or NIST (pH4.01, 6.86, 9.18) |
| Auto-Off | 8 minutes after last key pressed |
| Sensor Type | Standard pH Electrode (Round Glass Bulb) |
| Replacement Sensors | Flat Surface pH Electrode (Order Code: PHscan-F), Long-Reach pH Electrode (Order Code: PHscan-L) |
| Operating Temperature | 0~60°C, 32~140°F |
| Power Requirements | 3×1.5V "G13A" batteries |
| Battery Life | Approximately 150 hours |
| Dimensions | 185(L)×40(Dia.)mm |
| Weight | 100 grams |

PHscan20S pocket pH tester is equipped with a standard pH electrode ( Round glass bulb ) that used to measures the pH of non-viscous, non-high temperature liquids, e.g., tap water, drinking water, rainwater, etc. 
Features:
>Up to 3 points push-button calibration with auto-buffer recognition. 
>Selectable pH buffer standards (USA or NIST). 
>Automatic Temperature Compensation provides accurate readings over the entire pH range. 
>Hold function freezes the current displayed value for easy viewing and recording. 
>Auto-power off feature helps you effectively conserve battery life. 
>Setup menu lets user customizes pH buffer standards, calibration points, automatic or manual hold function to meet your personal preferences. 
>Reset feature allows user to resume all of the default settings. 
>Replaceable electrode reduces maintenance and replacement cost. 
>Waterproof feature to ensures complete protection in harsh environments.

Specifications:

| Model No. | PHscan20S |
| --- | --- |
| pH Range | -1.00~15.00pH |
| pH Accuracy | ±0.01pH |
| Calibration Points | 1, 2 or 3 points |
| Calibration Solutions | USA (pH4.01, 7.00, 10.01) or NIST (pH4.01, 6.86, 9.18) |
| Temperature Compensation | 0~60°C, 32~140°F, Automatic |
| Temperature Display | No |
| Auto-Off | Manual or Automatic (8 minutes after last key pressed) |
| Hold Function | Manual or Automatic endpoint |
| Reset Function | Yes |
| Sensor Type | Standard pH Electrode (Round Glass Bulb) |
| Replacement Sensors | Flat Surface pH Electrode (Order Code: PHscan-FT), Long-Reach pH Electrode (Order Code: PHscan-LT) |
| Operating Temperature | 0~60°C, 32~140°F |
| Power Requirements | 2×1.5V "AAA" batteries |
| Battery Life | Approximately 200 hours |
| Dimensions | 185(L)×40(Dia.)mm |
| Weight | 100 grams |

PHscan30S pocket pH tester is equipped with a standard pH electrode ( Round glass bulb ) that used to measures the pH of non-viscous, non-high temperature liquids, e.g., tap water, drinking water, rainwater, etc.

Features:
>Up to 3 points push-button calibration with auto-buffer recognition. 
>Selectable pH buffer standards ( USA/NIST ) and temperature units. 
>Manual temperature calibration provides accurate measured value. 
>Automatic Temperature Compensation ensures highly accurate measurements over the entire pH range. 
>Hold function immediately freezes the current displayed value. 
>Auto-power off feature helps you effectively conserve battery life. 
>Setup menu lets user customizes pH buffer standards, calibration points, temperature units, automatic or manual hold function to meet your personal preferences. 
>Reset feature allows user to resume all of the default settings. 
>Replaceable electrode reduces maintenance and replacement cost. 
>Waterproof feature to ensures complete protection in harsh environments.

Specifications:

| Model No. | PHscan30S |
| --- | --- |
| pH Range | -1.00~15.00pH |
| pH Accuracy | ±0.01pH |
| Calibration Points | 1, 2 or 3 points |
| Calibration Solutions | USA (pH4.01, 7.00, 10.01) or NIST (pH4.01, 6.86, 9.18) |
| Temperature Range | 0.0~60.0°C, 32.0~140.0°F |
| Temperature Accuracy | ±1°C |
| Temperature Calibration | Measuring value ±10°C |
| Temperature Compensation | 0~60°C, 32~140°F, Automatic |
| Auto-Off | Manual or Automatic (8 minutes after last key pressed) |
| Hold Function | Manual or Automatic endpoint |
| Reset Function | Yes |
| Sensor Type | Standard pH Electrode (Round Glass Bulb) |
| Replacement Sensors | Flat Surface pH Electrode (Order Code: PHscan-FT), Long-Reach pH Electrode (Order Code: PHscan-LT) |
| Operating Temperature | 0~60°C, 32~140°F |
| Power Requirements | 2×1.5V "AAA" batteries |
| Battery Life | Approximately 200 hours |
| Dimensions | 185(L)×40(Dia.)mm |
| Weight | 100 grams |

PHscan10F pocket pH tester is equipped with flat surface pH electrode that used to measures pH of semisolid substances, e.g., fruits, bread, creams, etc.

Features:

>2 points push-button calibration with auto-buffer recognition. 
>Hold function freezes the current displayed value for easy viewing and recording. 
>Auto-power off feature helps you effectively conserve battery life. 
>Replaceable electrode reduces maintenance and replacement cost. 
>Waterproof feature to ensures complete protection in harsh environments.

Specifications:

| Model No. | PHscan10F |
| --- | --- |
| pH Range | 0.0~14.0pH |
| pH Accuracy | ±0.1pH |
| Calibration Points | 2 points |
| Calibration Solutions | USA (pH4.01, 7.00, 10.01) or NIST (pH4.01, 6.86, 9.18) |
| Auto-Off | 8 minutes after last key pressed |
| Sensor Type | Flat Surface pH Electrode |
| Replacement Sensors | Standard pH Electrode (Order Code: PHscan-S), Long-Reach pH Electrode (Order Code: PHscan-L) |
| Operating Temperature | 0~60°C, 32~140°F |
| Power Requirements | 3×1.5V "G13A" batteries |
| Battery Life | Approximately 150 hours |
| Dimensions | 185(L)×40(Dia.)mm |
| Weight | 100 grams |

PHscan20F pocket pH tester is equipped with flat surface pH electrode that used to measures pH of semisolid substances, e.g., fruits, bread, creams, etc.

Features:
>Up to 3 points push-button calibration with auto-buffer recognition. 
>Selectable pH buffer standards (USA or NIST). 
>Automatic Temperature Compensation provides accurate readings over the entire pH range. 
>Hold function freezes the current displayed value for easy viewing and recording. 
>Auto-power off feature helps you effectively conserve battery life. 
>Setup menu lets user customizes pH buffer standards, calibration points, automatic or manual hold function to meet your personal preferences. 
>Reset feature allows user to resume all of the default settings. 
>Replaceable electrode reduces maintenance and replacement cost. 
>Waterproof feature to ensures complete protection in harsh environments.

Specifications:

| Model No. | PHscan20F |
| --- | --- |
| pH Range | -1.00~15.00pH |
| pH Accuracy | ±0.01pH |
| Calibration Points | 1, 2 or 3 points |
| Calibration Solutions | USA (pH4.01, 7.00, 10.01) or NIST (pH4.01, 6.86, 9.18) |
| Temperature Compensation | 0~60°C, 32~140°F, Automatic |
| Temperature Display | No |
| Auto-Off | Manual or Automatic (8 minutes after last key pressed) |
| Hold Function | Manual or Automatic endpoint |
| Reset Function | Yes |
| Sensor Type | Flat Surface pH Electrode |
| Replacement Sensors | Standard pH Electrode (Order Code: PHscan-ST), Long-Reach pH Electrode (Order Code: PHscan-LT) |
| Operating Temperature | 0~60°C, 32~140°F |
| Power Requirements | 2×1.5V "AAA" batteries |
| Battery Life | Approximately 200 hours |
| Dimensions | 185(L)×40(Dia.)mm |
| Weight | 100 grams |

PHscan30F pocket pH tester is equipped with flat surface pH electrode that used to measures pH of semisolid substances, e.g., fruits, bread, creams, etc.

Features:
>Up to 3 points push-button calibration with auto-buffer recognition. 
>Selectable pH buffer standards ( USA/NIST ) and temperature units. 
>Manual temperature calibration provides accurate measured value. 
>Automatic Temperature Compensation ensures highly accurate measurements over the entire pH range. 
>Hold function immediately freezes the current displayed value. 
>Auto-power off feature helps you effectively conserve battery life. 
>Setup menu lets user customizes pH buffer standards, calibration points, temperature units, automatic or manual hold function to meet your personal preferences. 
>Reset feature allows user to resume all of the default settings. 
>Replaceable electrode reduces maintenance and replacement cost. 
>Waterproof feature to ensures complete protection in harsh environments.

Specifications:

| Model No. | PHscan30F |
| --- | --- |
| pH Range | -1.00~15.00pH |
| pH Accuracy | ±0.01pH |
| Calibration Points | 1, 2 or 3 points |
| Calibration Solutions | USA (pH4.01, 7.00, 10.01) or NIST (pH4.01, 6.86, 9.18) |
| Temperature Range | 0.0~60.0°C, 32.0~140.0°F |
| Temperature Accuracy | ±1°C |
| Temperature Calibration | Measuring value ±10°C |
| Temperature Compensation | 0~60°C, 32~140°F, Automatic |
| Auto-Off | Manual or Automatic (8 minutes after last key pressed) |
| Hold Function | Manual or Automatic endpoint |
| Reset Function | Yes |
| Sensor Type | Flat Surface pH Electrode |
| Replacement Sensors | Standard pH Electrode (Order Code: PHscan-ST) Long-Reach pH Electrode (Order Code: PHscan-LT) |
| Operating Temperature | 0~60°C, 32~140°F |
| Power Requirements | 2×1.5V "AAA" batteries |
| Battery Life | Approximately 200 hours |
| Dimensions | 185(L)×40(Dia.)mm |
| Weight | 100 grams |

PHscan10L pocket pH tester is equipped with a long-reach pH electrode that used to measures the liquids in the test tube.

Features:
>2 points push-button calibration with auto-buffer recognition. 
>Hold function freezes the current displayed value for easy viewing and recording. 
>Auto-power off feature helps you effectively conserve battery life. 
>Replaceable electrode reduces maintenance and replacement cost. 
>Waterproof feature to ensures complete protection in harsh environments.

Specifications:

| Model No. | PHscan10L |
| --- | --- |
| pH Range | 0.0~14.0pH |
| pH Accuracy | ±0.1pH |
| Calibration Points | 2 points |
| Calibration Solutions | USA (pH4.01, 7.00, 10.01) or NIST (pH4.01, 6.86, 9.18) |
| Auto-Off | 8 minutes after last key pressed |
| Sensor Type | Long-Reach pH Electrode |
| Replacement Sensors | Standard pH Electrode (Order Code: PHscan-S), Flat Surface pH Electrode (Order Code: PHscan-F) |
| Operating Temperature | 0~60°C, 32~140°F |
| Power Requirements | 3×1.5V "G13A" batteries |
| Battery Life | Approximately 150 hours |
| Dimensions | 185(L)×40(Dia.)mm |
| Weight | 100 grams |

PHscan20L pocket pH tester is equipped with a long-reach pH electrode that used to measures the liquids in the test tube.

Features:
>Up to 3 points push-button calibration with auto-buffer recognition. 
>Selectable pH buffer standards (USA or NIST). 
>Automatic Temperature Compensation provides accurate readings over the entire pH range. 
>Hold function freezes the current displayed value for easy viewing and recording. 
>Auto-power off feature helps you effectively conserve battery life. 
>Setup menu lets user customizes pH buffer standards, calibration points, automatic or manual hold function to meet your personal preferences. 
>Reset feature allows user to resume all of the default settings. 
>Replaceable electrode reduces maintenance and replacement cost. 
>Waterproof feature to ensures complete protection in harsh environments.

Specifications:

| Model No. | PHscan20L |
| --- | --- |
| pH Range | -1.00~15.00pH |
| pH Accuracy | ±0.01pH |
| Calibration Points | 1, 2 or 3 points |
| Calibration Solutions | USA (pH4.01, 7.00, 10.01) or NIST (pH4.01, 6.86, 9.18) |
| Temperature Compensation | 0~60°C, 32~140°F, Automatic |
| Temperature Display | No |
| Auto-Off | Manual or Automatic (8 minutes after last key pressed) |
| Hold Function | Manual or Automatic endpoint |
| Reset Function | Yes |
| Sensor Type | Long-Reach pH Electrode |
| Replacement Sensors | Standard pH Electrode (Order Code: PHscan-ST) Flat Surface pH Electrode (Order Code: PHscan-FT) |
| Operating Temperature | 0~60°C, 32~140°F |
| Power Requirements | 2×1.5V "AAA" batteries |
| Battery Life | Approximately 200 hours |
| Dimensions | 185(L)×40(Dia.)mm |
| Weight | 100 grams |

PHscan30L pocket pH tester is equipped with a long-reach pH electrode that used to measures the liquids in the test tube.
Features:
>Up to 3 points push-button calibration with auto-buffer recognition. 
>Selectable pH buffer standards ( USA/NIST ) and temperature units. 
>Manual temperature calibration provides accurate measured value. 
>Automatic Temperature Compensation ensures highly accurate measurements over the entire pH range. 
>Hold function immediately freezes the current displayed value. 
>Auto-power off feature helps you effectively conserve battery life. 
>Setup menu lets user customizes pH buffer standards, calibration points, temperature units, automatic or manual hold function to meet your personal preferences. 
>Reset feature allows user to resume all of the default settings. 
>Replaceable electrode reduces maintenance and replacement cost. 
>Waterproof feature to ensures complete protection in harsh environments.

Specifications:

| Model No. | PHscan30L |
| --- | --- |
| pH Range | -1.00~15.00pH |
| pH Accuracy | ±0.01pH |
| Calibration Points | 1, 2 or 3 points |
| Calibration Solutions | USA (pH4.01, 7.00, 10.01) or NIST (pH4.01, 6.86, 9.18) |
| Temperature Range | 0.0~60.0°C, 32.0~140.0°F |
| Temperature Accuracy | ±1°C |
| Temperature Calibration | Measuring value ±10°C |
| Temperature Compensation | 0~60°C, 32~140°F, Automatic |
| Auto-Off | Manual or Automatic (8 minutes after last key pressed) |
| Hold Function | Manual or Automatic endpoint |
| Reset Function | Yes |
| Sensor Type | Long-Reach pH Electrode |
| Replacement Sensors | Standard pH Electrode (Order Code: PHscan-ST), Flat Surface pH Electrode (Order Code: PHscan-FT) |
| Operating Temperature | 0~60°C, 32~140°F |
| Power Requirements | 2×1.5V "AAA" batteries |
| Battery Life | Approximately 200 hours |
| Dimensions | 185(L)×40(Dia.)mm |
| Weight | 100 grams |

PHscan40 BNC pocket pH tester is equipped with a standard BNC connector, which can uses any pH electrode with BNC plug.
Features:
>Up to 3 points push-button calibration with auto-buffer recognition. 
>Selectable pH buffer standards ( USA/NIST ) and temperature units. 
>Manual Temperature Compensation ensures high accuracy of measurements. 
>Hold function freezes the current displayed value for easy viewing and recording. 
>Auto-power off feature helps you effectively conserve battery life. 
>Setup menu lets user customizes pH buffer standards, calibration points, temperature units, automatic or manual hold function to meet your personal preferences. 
>Reset feature allows user to resume all of the default settings. 
>BNC connector can connect to any combination pH electrode. 
>Waterproof feature to ensures complete protection in harsh environments.

Specifications:

| Model No. | PHscan40BNC |
| --- | --- |
| pH Range | -1.00~15.00pH |
| pH Accuracy | ±0.01pH |
| Calibration Points | 1, 2 or 3 points |
| Calibration Solutions | USA (pH4.01, 7.00, 10.01) or NIST (pH4.01, 6.86, 9.18) |
| Temperature Compensation | 0~100°C, 32~212°F, Manual |
| Auto-Off | Manual or Automatic (8 minutes after last key pressed) |
| Hold Function | Manual or Automatic endpoint |
| Reset Function | Yes |
| Connector | BNC |
| Operating Temperature | 0~60°C, 32~140°F |
| Power Requirements | 2×1.5V "AAA" batteries |
| Battery Life | Approximately 200 hours |
| Dimensions | 185(L)×40(Dia.)mm |
| Weight | 100 grams |

# PHS-W SERIES MICROPROCESSOR pH/mV METER(CE marked)

Features:

PHS-W series is an easy-use basic pH meter designed for daily testing and controls are required. This series pH meter includes model PHS-25CW, PHS-3CW and PHS-3BW, it widely used for water quality research, industry and education applications.

>Automatic Calibration: 
The meters is capable of calibrating up to 3 points using USA or NIST pH standard buffer. Press the CAL key to enter calibration mode and immerse pH sensor into indicated calibration solutions, press ENTER key and meter is automatically calibrated.

>Auto-Buffer Recognition: 
During calibration, if the calibration solution does not match the meter’s indicated value, an ERROR message is displayed. After calibration, the percentage slope of the electrode is displayed before the meter returns to measurement mode. Per the electrode slopes, you can decides whether to replace the pH electrode. 　 

>Automatic or Manual Temperature Compensation: 
The meters provides manual or automatic temperature compensation mode for optimum accuracy under variable temperature conditions. 　 

>Fluid Resistant Housing and Swivel Electrode Holder: 
The integrated plastic housing and keypad is sealed to protect against accidental spills. The electrode holder arm is rapidly switched to both sides and swivels and articulates for convenient use and positioning.

Specification:

| Model No. | PHS-25CW | PHS-3CW | PHS-3BW |
| --- | --- | --- | --- |
| pH Range | 0.00~14.00pH | 0.00~14.00pH | 0.00~14.00pH |
| pH Accuracy | ±0.05pH | ±0.01pH | ±0.01pH |
| mV Range | 0~±1999mV | 0~±1999mV | 0~±1999mV |
| mV Accuracy | ±10mV | ±2mV | ±2mV |
| Temperature Range | --- | --- | 0~100℃ |
| Temperature Accuracy | --- | --- | ±1℃ |
| Temperature Compensation | 0~100℃ Manual | 0~100℃ Manual | 0~100℃ Manual or Automatic |
| Calibration Points | 2 Points |
| pH Standard Solution | NIST, pH4.00/6.86/9.18 or USA, pH4.01/7.00/10.01 |
| Power Requirement | 9V DC, Using AC adapters, 220V/50Hz |
| Dimension | 210(L)mm×205(W)mm×65(H)mm |
| Weight | 1.7kg |

92 Series Benchtop pH/mV Meter

210 is an easy-use benchtop pH meter designed for daily testing and controls are required.

Features:
>Large backlit LCD display shows mode indicators and help messages. 
>Up to 3 points push-button calibration with auto-buffer recognition. 
>Selectable pH buffer standards and temperature units. 
>Automatically calculates and displays electrode slope after calibration. 
>Automatic Temperature Compensation (ATC) ensures highly accurate measurements over the entire range. 
>Automatic endpoint function freezes the stable measured values for easy reading and recording data. 
>Manual temperature calibration provides accurate temperature value. 
>Help message as a operational guide to helps you understand how to use meter.
>Setup menu lets user customizes buffer standards, calibration points, temperature units, automatic or manual hold function, auto-off feature to meet personal preferences. 
>Reset function can resumes all settings to factory default values .

Specifications:

| Model No. | 210 |
| --- | --- |
| pH Range | -1.00~15.00pH |
| pH Accuracy | ±0.01pH |
| mV Range | -1000~1000mV |
| mV Accuracy | ±1mV |
| Calibration Points | 1, 2 or 3 points |
| Calibration Solutions | USA (pH4.01/7.00/10.01) or NIST (pH4.01/6.86/9.18) |
| Temperature Range | 0~105°C, 32~221°F |
| Temperature Accuracy | ±1°C |
| Temperature Calibration | Manual |
| Temperature Compensation | 0~100°C, 32~212°F, Automatic or Manual |
| Auto-Off | Manual or Automatic (180 minutes after last key pressed) |
| Hold Function | Manual or Automatic endpoint |
| Reset Function | Yes |
| Connector | BNC |
| LCD Display | Custom Dual-Display LCD (135×75mm) |
| Power Requirements | DC9V, using AC adapters, 220VAC/50Hz |
| Dimensions | 210(L)×205(W)×75(H)mm |
| Weight | 1.2kg |

920 is a high precision pH meter which is equipped with large backlit LCD display. The meter can displays many useful prompt messages to helps you quickly and easily measuring the samples.
Features:
>During the pH mode, Up to 5 points push-button calibration with auto- buffer recognition. 
>Selectable pH buffer standards and temperature units. 
>Automatically calculates and displays electrode slope after calibration. 
>Automatic Temperature Compensation (ATC) ensures highly accurate measurements over the entire range. 
>Calibration due reminder prompts you to calibrate the meter regularly. 
>During ORP mode, Single point offset calibration allows user adjusts displayed value to a known standard. 
>Absolute or Relative millivolt (R.mV) measurement provides accurate ORP readings. 
>Automatic endpoint function freezes the stable measured values for easy reading and recording data. 
>Manual temperature calibration provides accurate temperature value. 
>Help message as a operational guide to helps you understand how to use meter.
>Setup menu lets user customizes buffer standards, calibration points, stability conditions, resolution, temperature units, date and time to meet measurement requirements. 
>Reset function can resumes all settings to factory default values. 
>Expanded memory stores and recalls up to 500 readings. 
>Built-in real-time clock stamps stored data to meets GLP standards. 
>Stored data can be transferred into computer via USB communication interface.

Specifications:

| Model No. | 920 |
| --- | --- |
| pH Range | -2.000~20.000pH |
| pH Accuracy | ±0.002pH |
| Resolution | 0.001, 0.01, 0.1pH, Selectable |
| mV Range | -1999.9~1999.9mV |
| mV Accuracy | ±0.2mV |
| Resolution | 0.1, 1mV, Selectable |
| Calibration Points | Up to 5 points |
| Calibration Solutions | USA(pH1.68/4.01/7.00/10.01/12.45), NIST(pH1.68/4.01/6.86/9.18/12.45), DIN (pH1.09/4.65/6.79/9.23/ 12.75) |
| Temperature Range | 0~105°C, 32~221°F |
| Temperature Accuracy | ±0.5°C, ±0.9°F |
| Temperature Calibration | Manual |
| Temperature Compensation | 0~100°C, 32~212°F, Automatic or Manual |
| Auto-Off | Manual or Automatic (10, 20, 30 minutes after last key pressed, Selectable) |
| Hold Function | Manual or Automatic endpoint |
| Stability Conditions | Low or High, Selectable |
| Calibration due reminder | 1 to 30 days or Off |
| Reset Function | Yes |
| Memory | 500 data sets with Date/Time stamping |
| Output | USB Communication Interface |
| Connector | BNC |
| LCD Display | Custom dual-display LCD (130×110mm) |
| Power Requirements | DC5V, using AC adapters, 220VAC/50Hz |
| Dimensions | 210(L)×188(W)×60(H)mm |
| Weight | 1.2kg |

930 is a high accuracy meter used for measuring the ion concentration, ORP and pH values of liquids. The meter widely used in environmental studies, chemical labs, swimming pools, spas to monitor the chemical reaction of water. 

Features:

>During the pH mode, Up to 5 points push-button calibration with auto- buffer recognition. 
>Selectable pH buffer standards and temperature units. 
>Automatically calculates and displays electrode slope after calibration. 
>During ORP mode, Single point offset calibration allows user adjusts displayed value to a known standard. 
>Absolute or Relative millivolt (R.mV) measurement provides accurate ORP readings. 
>During the ion mode, 2 to 5 points push-button calibration from low to high concentrations. 
>Selectable multiple concentration units, including ppm, mg/L and mol/L. 
>Direct readout ion concentration simplifies the elaborate measurement process. 
>Automatic Temperature Compensation (ATC) ensures highly accurate measurements over the entire range. 
>Automatic endpoint function freezes the stable measured values for easy reading and recording data. 
>Calibration due reminder prompts you to calibrate the meter regularly. 
>Manual temperature calibration provides accurate temperature value. 
>Help message as a operational guide to helps you understand how to use meter.
>Setup menu lets user customizes buffer standards, calibration points, stability conditions, resolution, measurement units, date and time to meet measurement requirements. 
>Reset function can resumes all settings to factory default values. 
>Expanded memory stores and recalls up to 500 readings. 
>Built-in real-time clock stamps stored data to meets GLP standards. 
>Stored data can be transferred into computer via USB communication interface.

Specifications:

| Model No. | 930 |
| --- | --- |
| pH Range | -2.000~20.000pH |
| pH Accuracy | ±0.002pH |
| Resolution | 0.001, 0.01, 0.1pH, Selectable |
| Calibration Points | Up to 5 points |
| Calibration Solutions | USA(pH1.68/4.01/7.00/10.01/12.45), NIST(pH1.68/4.01/6.86/9.18/12.45), DIN (pH1.09/4.65/6.79/9.23/ 12.75) |
| Ion Concentration Range | 0.001~19999ppm, mg/L, mol/L (Depending on measuring range of Ion Selective Electrode) |
| Ion Concentration Accuracy | ±0.5% Full Scale (Monovalent), ±1% Full Scale (Divalent) |
| Calibration Points | 2 to 5 points |
| Calibration Solutions | 0.001, 0.01, 0.1, 1, 10, 100, 1000, 10000ppm |
| mV Range | -1999.9~1999.9mV |
| mV Accuracy | ±0.2mV |
| Resolution | 0.1, 1mV, Selectable |
| Temperature Range | 0~105°C, 32~221°F |
| Temperature Accuracy | ±0.5°C, ±0.9°F |
| Temperature Calibration | Manual |
| Temperature Compensation | 0~100°C, 32~212°F, Automatic or Manual |
| Auto-Off | Manual or Automatic (10, 20, 30 minutes after last key pressed, Selectable) |
| Hold Function | Manual or Automatic endpoint |
| Stability Conditions | Low or High, Selectable |
| Calibration due reminder | 1 to 30 days or Off |
| Reset Function | Yes |
| Memory | 500 data sets with Date/Time stamping |
| Output | USB Communication Interface |
| Connector | BNC |
| LCD Display | Custom dual-display LCD (130×110mm) |
| Power Requirements | DC5V, using AC adapters, 220VAC/50Hz |
| Dimensions | 210(L)×188(W)×60(H)mm |
| Weight | 1.2kg |

Portable pH/mV Meter

220 is an economical portable pH/mV meter designed for outdoor applications, which is equipped with a large LCD and a standard BNC connecter. The meter is capable of connecting the various combination pH electrodes to measures pH values of solutions. 

Features:

>2 points push-button calibration with auto-buffer recognition. 
>Automatically calculates and displays electrode slopes that helps you decide whether to replace pH electrode. 
>Selectable either temperature units between degrees Celsius (°C) and degrees Fahrenheit (°F). 
>Automatic Temperature Compensation (ATC) ensures highly accurate measurements over the entire pH range. 
>Manual temperature calibration provides accurate temperature values 
>Hold function freezes the current displayed values for easy viewing and recording.
>Help message as a operational guide to helps you understand how to use meter. 
>Setup menu allows user customizes temperature units, date and time to meet measurement requirements. 
>Expanded memory stores and recalls up to 50 readings. 
>Built-in real-time clock stamps stored data to meets GLP standards. 
>Stored data can be transferred into computer via USB communication interface.

Specifications:

| Model No. | 220 |
| --- | --- |
| pH Range | -2.00~16.00pH |
| pH Accuracy | ±0.01pH |
| mV Range | -1999~1999mV |
| mV Accuracy | ±1mV |
| Calibration Points | 2 points |
| Calibration Solutions | USA (pH4.01, 7.00, 10.01) |
| Temperature Range | 0~100°C, 32~212°F |
| Temperature Accuracy | ±1°C |
| Temperature Calibration | Manual |
| Temperature Compensation | 0~100°C, 32~212°F, Automatic or Manual |
| Hold Function | Manual |
| Memory | 50 data sets with Date/Time stamping |
| Output | USB Communication Interface |
| Connector | BNC |
| Power Requirements | 1×9V/800mA battery |
| Battery Life | Approximately 150 hours |
| Dimensions | 185(L)×88(W)×32(H)mm |
| Weight | 300 grams |

221 is a high performance portable pH/ORP meter designed for outdoor applications. The meter contains a built-in setup menu that provides many advanced and useful options to improves accuracy of measurements and simplify operations. 

Features:
>During the pH mode, Up to 5 points push-button calibration with auto- buffer recognition. 
>Selectable pH buffer standards and temperature units. 
>Automatically calculates and displays electrode slope after calibration. 
>Automatic Temperature Compensation (ATC) ensures highly accurate measurements over the entire range. 
>Calibration due reminder prompts you to calibrate the meter regularly. 
>During ORP mode, Single point offset calibration allows user adjusts displayed value to a known standard. 
>Absolute or Relative millivolt (R.mV) measurement provides accurate ORP readings. 
>Automatic endpoint function freezes the stable measured values for easy reading and recording data. 
>Manual temperature calibration provides accurate temperature value. 
>Help message as a operational guide to helps you understand how to use meter.
>Setup menu lets user customizes buffer standards, calibration points, stability conditions, resolution, temperature units, date and time to meet measurement requirements. 
>Reset function can resumes all settings to factory default values. 
>Expanded memory stores and recalls up to 500 readings. 
>Built-in real-time clock stamps stored data to meets GLP standards. 
>Stored data can be transferred into computer via USB communication interface.

Specifications:

| Model No. | 221 |
| --- | --- |
| pH Range | -2.000~20.000pH |
| pH Accuracy | ±0.002pH |
| Resolution | 0.001, 0.01, 0.1pH, Selectable |
| mV Range | -1999.9~1999.9mV |
| mV Accuracy | ±0.2mV |
| Resolution | 0.1, 1mV, Selectable |
| Calibration Points | Up to 5 points |
| Calibration Solutions | USA(pH1.68/4.01/7.00/10.01/12.45), NIST(pH1.68/4.01/6.86/9.18/12.45), DIN (pH1.09/4.65/6.79/9.23/ 12.75) |
| Temperature Range | 0~105°C, 32~221°F |
| Temperature Accuracy | ±0.5°C, ±0.9°F |
| Temperature Calibration | Manual |
| Temperature Compensation | 0~100°C, 32~212°F, Automatic or Manual |
| Auto-Off | Manual or Automatic (10, 20, 30 minutes after last key pressed, Selectable) |
| Hold Function | Manual or Automatic endpoint |
| Stability Conditions | Low or High, Selectable |
| Calibration due reminder | 1 to 30 days or Off |
| Reset Function | Yes |
| Memory | 500 data sets with Date/Time stamping |
| Output | USB Communication Interface |
| Connector | BNC |
| Power Requirements | 3×1.5V "AA" batteries |
| Battery Life | Approximately 150 hours |
| Dimensions | 170(L)×85(W)×30(H)mm |
| Weight | 300 grams |

320 is a multi-parameter ion meter used for measuring the ion concentration and pH value of liquids. The meter is equipped with a BNC connecter that can connects various combination Ion Selective Electrodes. 

Features:

>During the pH mode, Up to 5 points push-button calibration with auto- buffer recognition. 
>Selectable pH buffer standards and temperature units. 
>Automatically calculates and displays electrode slope after calibration. 
>During ORP mode, Single point offset calibration allows user adjusts displayed value to a known standard. 
>Absolute or Relative millivolt (R.mV) measurement provides accurate ORP readings. 
>During the ion mode, 2 to 5 points push-button calibration from low to high concentrations. 
>Selectable multiple concentration units, including ppm, mg/L and mol/L. 
>Direct readout ion concentration simplifies the elaborate measurement process. 
>Automatic Temperature Compensation (ATC) ensures highly accurate measurements over the entire range. 
>Automatic endpoint function freezes the stable measured values for easy reading and recording data. 
>Calibration due reminder prompts you to calibrate the meter regularly. 
>Manual temperature calibration provides accurate temperature value. 
>Help message as a operational guide to helps you understand how to use meter.
>Setup menu lets user customizes buffer standards, calibration points, stability conditions, resolution, measurement units, date and time to meet measurement requirements. 
>Reset function can resumes all settings to factory default values. 
>Expanded memory stores and recalls up to 500 readings. 
>Built-in real-time clock stamps stored data to meets GLP standards. 
>Stored data can be transferred into computer via USB communication interface.

Specifications:

| Model No. | 320 |
| --- | --- |
| pH Range | -2.000~20.000pH |
| pH Accuracy | ±0.002pH |
| Resolution | 0.001, 0.01, 0.1pH, Selectable |
| Calibration Points | Up to 5 points |
| Calibration Solutions | USA(pH1.68/4.01/7.00/10.01/12.45), NIST(pH1.68/4.01/6.86/9.18/12.45), DIN (pH1.09/4.65/6.79/9.23/ 12.75) |
| Ion Concentration Range | 0.001~19999ppm, mg/L or mol/L (Depending on measuring range of Ion Selective Electrode) |
| Ion Concentration Accuracy | ±0.5% Full Scale (Monovalent), ±1% Full Scale (Divalent) |
| Calibration Points | 2 to 5 points |
| Calibration Solutions | 0.001, 0.01, 0.1, 1, 10, 100, 1000, 10000ppm |
| mV Range | -1999.9~1999.9mV |
| mV Accuracy | ±0.2mV |
| Resolution | 0.1, 1mV, Selectable |
| Temperature Range | 0~105°C, 32~221°F |
| Temperature Accuracy | ±0.5°C, ±0.9°F |
| Temperature Calibration | Manual |
| Temperature Compensation | 0~100°C, 32~212°F, Automatic or Manual |
| Auto-Off | Manual or Automatic (10, 20, 30 minutes after last key pressed, Selectable) |
| Hold Function | Manual or Automatic endpoint |
| Stability Conditions | Low or High, Selectable |
| Calibration due reminder | 1 to 30 days or Off |
| Reset Function | Yes |
| Memory | 500 data sets with Date/Time stamping |
| Output | USB Communication Interface |
| Connector | BNC |
| Power Requirements | 3×1.5V "AA" batteries |
| Battery Life | Approximately 150 hours |
| Dimensions | 170(L)×85(W)×30(H)mm |
| Weight | 300 grams |